## Slide 1: Computer Organization and Architecture Designing for Performance
Chapter 7
External Memory
11th Edition, Global Edition

## Slide 2: Magnetic Disk
A disk is a circular platter constructed of nonmagnetic material, called the substrate, coated with a magnetizable material
  Traditionally the substrate has been an aluminium or aluminium alloy material
  Recently glass substrates have been introduced
Benefits of the glass substrate:
  Improvement in the uniformity of the magnetic film surface to increase disk reliability
  A significant reduction in overall surface defects to help reduce read-write errors
  Ability to support lower fly heights
  Better stiffness to reduce disk dynamics
  Greater ability to withstand shock and damage
Notes: A disk is a circular platter constructed of nonmagnetic material, called the substrate,
coated with a magnetizable material. Traditionally, the substrate has been an aluminum
or aluminum alloy material. More recently, glass substrates have been introduced.
The glass substrate has a number of benefits, including the following:
• Improvement in the uniformity of the magnetic film surface to increase disk
reliability
• A significant reduction in overall surface defects to help reduce read-write errors
• Ability to support lower fly heights (described subsequently)
• Better stiffness to reduce disk dynamics
• Greater ability to withstand shock and damage

## Slide 3: Magnetic Read and Write Mechanisms
The write mechanism exploits the fact that electricity flowing through a coil produces a magnetic field
Electric pulses are sent to the write head and the resulting magnetic patterns are recorded on the surface below, with different patterns for positive and negative currents
The write head itself is made of easily magnetizable material and is in the shape of a rectangular doughnut with a gap along one side and a few turns of conducting wire along the opposite side
An electric current in the wire induces a magnetic field across the gap, which in turn magnetizes a small area of the recording medium
Reversing the direction of the current reverses the direction of the magnetization on the recording medium
During a read or write operation the head is stationary while the platter rotates beneath it
In many systems there are two heads, a read head and a write head
Data are recorded on and later retrieved from the disk via a conducting coil named the head
Notes: Data are recorded on and later retrieved from the disk via a conducting coil named
the head; in many systems, there are two heads, a read head and a write head. During
a read or write operation, the head is stationary while the platter rotates beneath it.
The write mechanism exploits the fact that electricity flowing through a coil
produces a magnetic field. Electric pulses are sent to the write head, and the resulting
magnetic patterns are recorded on the surface below, with different patterns for
positive and negative currents. The write head itself is made of easily magnetizable
material and is in the shape of a rectangular doughnut with a gap along one side and
a few turns of conducting wire along the opposite side (Figure 7.1). An electric current
in the wire induces a magnetic field across the gap, which in turn magnetizes a
small area of the recording medium. Reversing the direction of the current reverses
the direction of the magnetization on the recording medium.
The traditional read mechanism exploits the fact that a magnetic field moving
relative to a coil produces an electrical current in the coil. When the surface of the
disk passes under the head, it generates a current of the same polarity as the one
already recorded. The structure of the head for reading is in this case essentially
the same as for writing and therefore the same head can be used for both. Such
single heads are used in floppy disk systems and in older rigid disk systems.
Contemporary rigid disk systems use a different read mechanism, requiring
a separate read head, positioned for convenience close to the write head. The read
head consists of a partially shielded magnetoresistive (MR) sensor. The MR material
has an electrical resistance that depends on the direction of the magnetization of
the medium moving under it. By passing a current through the MR sensor, resistance
changes are detected as voltage signals. The MR design allows higher-frequency
operation, which equates to greater storage densities and operating speeds.

## Slide 4: Figure 7.1 Inductive Write/Magnetoresistive Read Head
Notes: Figure 7.1. Inductive Write/Magnetoresistive Read Head

## Slide 5: Figure 7.2 Disk Data Layout
Notes: The head is a relatively small device capable of reading from or writing to a portion
of the platter rotating beneath it. This gives rise to the organization of data on the
platter in a concentric set of rings, called tracks. Each track is the same width as the
head. There are thousands of tracks per surface.
Figure 7.2 depicts this data layout. Adjacent tracks are separated by intertrack
gaps. This prevents, or at least minimizes, errors due to misalignment of the head
or simply interference of magnetic fields. Data are transferred to and from the disk
in sectors. There are typically hundreds of sectors per track, and these may be of
either fixed or variable length. In most contemporary systems, fixed-
length sectors are used. To avoid imposing unreasonable precision requirements on
the system, adjacent sectors are separated by intersector gaps.

## Slide 6: Figure 7.3 Comparison of Disk Layout Methods
Notes: A bit near the center of a rotating disk travels past a fixed point (such as a read–
write head) slower than a bit on the outside. Therefore, some way must be found
to compensate for the variation in speed so that the head can read all the bits at the
same rate. This can be done by defining a variable spacing between bits of information
recorded in locations on the disk, in a way that the outermost tracks have sectors with
bigger spacing. The information can then be scanned at the same rate by rotating the
disk at a fixed speed, known as the constant angular velocity (CAV). Figure 7.3a shows
the layout of a disk using CAV. The disk is divided into a number of pie-shaped
sectors and into a series of concentric tracks. The advantage of using CAV is that individual
blocks of data can be directly addressed by track and sector. To move the head from its
current location to a specific address, it only takes a short movement of the head to a
specific track and a short wait for the proper sector to spin under the head. The disadvantage
of CAV is that the amount of data that can be stored on the long outer tracks is
the same as what can be stored on the short inner tracks.
Because the density, in bits per linear inch, increases in moving from the outermost
track to the innermost track, disk storage capacity in a straightforward CAV
system is limited by the maximum recording density that can be achieved on the
innermost track. To maximize storage capacity, it would be preferable to have the
same linear bit density on each track. This would require unacceptably complex
circuitry. Modern hard disk systems use a simpler technique, which approximates
equal bit density per track, known as multiple zone recording (MZR), in which
the surface is divided into a number of concentric zones (16 is typical). Each zone
contains a number of contiguous tracks, typically in the thousands. Within a zone,
the number of bits per track is constant. Zones farther from the center contain more
bits (more sectors) than zones closer to the center. Zones are defined in such a way
that the linear bit density is approximately the same on all tracks of the disk. MZR
allows for greater overall storage capacity at the expense of somewhat more complex
circuitry. As the disk head moves from one zone to another, the length (along
the track) of individual bits changes, causing a change in the timing for reads and
writes.
Figure 7.3b is a simplified MZR layout, with 15 tracks organized into 5 zones.
The innermost two zones have two tracks each, with each track having nine sectors;
the next zone has 3 tracks, each with 12 sectors; and the outermost 2 zones have 4
tracks each, with each track having 16 sectors.

## Slide 7: Figure 7.4 Legacy and Advanced Sector Formats
Notes: Some means is needed to locate sector positions within a track. Clearly, there
must be some starting point on the track and a way of identifying the start and end
of each sector. These requirements are handled by means of control data recorded
on the disk. Thus, the disk is formatted with some extra data used only by the disk
drive and not accessible to the user.
Figure 7.4. shows two common sector formats used in contemporary hard disk
drives. The standard format used for many years divided the track into sectors, each containing
512 bytes of data. Each sector also includes control information useful to the disk
controller. The structure of the sector layout for this format consists of the following:
■ Gap: Separates sectors.
■ Sync: Indicates the beginning of the sector and provides timing alignment.
■ Address mark: Contains data to identify the sector’s number and location. It
also provides status about the sector itself.
■ Data: The 512 bytes of user data.
■ Error correction code (ECC): Used to correct data that might be damaged in
the reading and writing process.
Although this format has served the industry well for many years, it has
become increasingly inadequate for two reasons:
1. Applications common in modern computing systems use much greater
amounts of data and manage the data in large blocks. Compared to these
requirements, the small blocks of traditional sector formatting devote a considerable
fraction of each sector to control information. The overhead consists
of 65 bytes, yielding a format efficiency of (512/512 + 65) ≈ 0.88.
2. Bit density on disks has increased substantially, so that each sector consumes less
physical space. Accordingly, a media defect or other error source can damage a
higher percentage of the total payload, requiring more error correction strength.
Accordingly, the industry has responded by standardizing a new Advanced
Format for a 4096-byte block, illustrated in Figure 7.4b. The leading overhead
remains at 15 bytes and the ECC is expanded to 100 bytes, yielding a format
efficiency of (4096/4096 + 115) ≈ 0.97, almost a 10% improvement in efficiency.
More significantly, doubling the ECC to 100 bytes enables the correction of longer
sequences of error bits.

## Slide 8: Table 7.1 Physical Characteristics of Disk Systems
Head Motion Fixed head (one per track) Movable head (one per surface) Disk Portability Nonremovable disk Removable disk Sides Single sided Double sided | Platters Single platter Multiple platter Head Mechanism Contact (floppy) Fixed gap Aerodynamic gap (Winchester)
Notes: Table 7.1 lists the major characteristics that differentiate among the various types
of magnetic disks.

## Slide 9: Characteristics
  Fixed-head disk
  One read-write head per track
  Heads are mounted on a fixed ridged arm that extends across all tracks
  Movable-head disk
  One read-write head
  Head is mounted on an arm
  The arm can be extended or retracted
  Non-removable disk
  Permanently mounted in the disk drive
  The hard disk in a personal computer is a non-removable disk
  Removable disk
  Can be removed and replaced with another disk
  Advantages:
    Unlimited amounts of data are available with a limited number of disk systems
    A disk may be moved from one computer system to another
  Floppy disks and ZIP cartridge disks are examples of removable disks
Double sided disk
  Magnetizable coating is applied to both sides of the platter
Notes: First, the head may either be fixed or movable with respect to
the radial direction of the platter. In a fixed-head disk, there is one read-write
head per track. All of the heads are mounted on a rigid arm that extends across
all tracks; such systems are rare today. In a movable-head disk, there is only one
read-write head. Again, the head is mounted on an arm. Because the head must
be able to be positioned above any track, the arm can be extended or retracted for
this purpose.
The disk itself is mounted in a disk drive, which consists of the arm, a spindle
that rotates the disk, and the electronics needed for input and output of binary data.
A non-removable disk is permanently mounted in the disk drive; the hard disk in
a personal computer is a non-removable disk. A removable disk can be removed
and replaced with another disk. The advantage of the latter type is that unlimited
amounts of data are available with a limited number of disk systems. Furthermore,
such a disk may be moved from one computer system to another. Floppy disks and
ZIP cartridge disks are examples of removable disks.
For most disks, the magnetizable coating is applied to both sides of the platter,
which is then referred to as double sided. Some less expensive disk systems use
single-sided disks.
Some disk drives accommodate multiple platters stacked vertically a fraction
of an inch apart. Multiple arms are provided (Figure 7.2). Multiple–platter disks
employ a movable head, with one read-write head per platter surface. All of the
heads are mechanically fixed so that all are at the same distance from the center of
the disk and move together. Thus, at any time, all of the heads are positioned over
tracks that are of equal distance from the center of the disk. The set of all the tracks
in the same relative position on the platter is referred to as a cylinder . This is illustrated
in Figure 7.2.

## Slide 10: Disk Classification
The head mechanism provides a classification of disks into three types
The head must generate or sense an electromagnetic field of sufficient magnitude to write and read properly
The narrower the head, the closer it must be to the platter surface to function
  A narrower head means narrower tracks and therefore greater data density
The closer the head is to the disk the greater the risk of error from impurities or imperfections
Winchester Heads
Used in sealed drive assemblies that are almost free of contaminants
Designed to operate closer to the disk’s surface than conventional rigid disk heads, thus allowing greater data density
Is actually an aerodynamic foil that rests lightly on the platter’s surface when the disk is motionless
  The air pressure generated by a spinning disk is enough to make the foil rise above the surface
Notes: Finally, the head mechanism provides a classification of disks into three types.
Traditionally, the read-write head has been positioned a fixed distance above the
platter, allowing an air gap. At the other extreme is a head mechanism that actually
comes into physical contact with the medium during a read or write operation. This
mechanism is used with the floppy disk, which is a small, flexible platter and the
least expensive type of disk.
To understand the third type of disk, we need to comment on the relationship
between data density and the size of the air gap. The head must generate or sense an
electromagnetic field of sufficient magnitude to write and read properly. The narrower
the head is, the closer it must be to the platter surface to function. A narrower
head means narrower tracks and therefore greater data density, which is desirable.
However, the closer the head is to the disk, the greater the risk of error from impurities
or imperfections. To push the technology further, the Winchester disk was
developed. Winchester heads are used in sealed drive assemblies that are almost
free of contaminants. They are designed to operate closer to the disk’s surface than
conventional rigid disk heads, thus allowing greater data density. The head is actually
an aerodynamic foil that rests lightly on the platter’s surface when the disk is
motionless. The air pressure generated by a spinning disk is enough to make the foil
rise above the surface. The resulting noncontact system can be engineered to use
narrower heads that operate closer to the platter’s surface than conventional rigid
disk heads.

## Slide 11: Figure 7.5 Timing of a Disk I/O Transfer
Notes: The actual details of disk I/O operation depend on the computer system, the operating
system, and the nature of the I/O channel and disk controller hardware. A
general timing diagram of disk I/O transfer is shown in Figure 7.5.

## Slide 12: Disk Performance Parameters
When the disk drive is operating the disk is rotating at constant speed
To read or write the head must be positioned at the desired track and at the beginning of the desired sector on the track
  Track selection involves moving the head in a movable-head system or electronically selecting one head on a fixed-head system
  Once the track is selected, the disk controller waits until the appropriate sector rotates to line up with the head
Seek time
  On a movable–head system, the time it takes to position the head at the track
  Rotational delay (latency time)
  The time it takes for the beginning of the sector to reach the head
  Bloc access time (access time)
  The sum of the seek time, the latency time, and the transfer time
  Transfer time
  Once the head is in position, the read or write operation is then
  performed as the sector moves under the head
  This is the data transfer portion of the operation
Notes: When the disk drive is operating, the disk is rotating at constant speed. To
read or write, the head must be positioned at the desired track and at the beginning
of the desired sector on that track. Track selection involves moving the head in a
movable-head system or electronically selecting one head on a fixed-head system.
On a movable-head system, the time it takes to position the head at the track is
known as seek time ts. In either case, once the track is selected, the disk controller
waits until the appropriate sector rotates to line up with the head. The time it takes
for the beginning of the sector to reach the head is known as rotational delay, or
latency time tL. Once the head is in position, the read or write operation is then performed
as the sector moves under the head; this is the data transfer portion of the operation; the time
required for the transfer is the transfer time tT. The sum of the
seek time, if any, the latency time, and the transfer time equals the bloc access time
tB, or simply access time.
In addition to the access time and transfer time, there are several queuing
delays normally associated with a disk I/O operation. When a process issues an I/O
request, it must first wait in a queue for the device to be available. At that time, the
device is assigned to the process. If the device shares a single I/O channel or a set
of I/O channels with other disk drives, then there may be an additional wait for the
channel to be available. At that point, the seek is performed to begin disk access.
In some high-end systems for servers, a technique known as rotational positional
sensing (RPS) is used. This works as follows: When the seek command has
been issued, the channel is released to handle other I/O operations. When the seek
is completed, the device determines when the data will rotate under the head. As
that sector approaches the head, the device tries to reestablish the communication
path back to the host. If either the control unit or the channel is busy with another
I/O, then the reconnection attempt fails and the device must rotate one whole
revolution before it can attempt to reconnect, which is called an RPS miss. This is
an extra delay element that must be added to the access time.
Seek time is the time required to move the disk arm to the required track.
It turns out that this is a difficult quantity to pin down. The seek time consists of two
key components: the initial startup time, and the time taken to traverse the tracks that
have to be crossed once the access arm is up to speed. Unfortunately, the traversal
time is not a linear function of the number of tracks, but includes a settling time (time
after positioning the head over the target track until track identification is confirmed).
A mean value of tS is typically provided by the manufacturer.
Much improvement comes from smaller and lighter disk components. Some
years ago, a typical disk was 14 inches (36 cm) in diameter, whereas the most
common size today is 3.5 inches (8.9 cm), reducing the distance that the arm has to
travel. A typical average seek time on contemporary hard disks is under 10 ms.
Disks, other than floppy disks, rotate at speeds ranging from
3600 rpm (for handheld devices such as digital cameras) up to, as of this writing,
20,000 rpm; at this latter speed, there is one revolution per 3 ms. Thus, on the
average, the latency time tL will be 1.5 ms.
It is clear that the order in which sectors are read from the disk has a tremendous
effect on I/O performance. In the case of file access in which multiple sectors
are read or written, we have some control over the way in which sectors of data are
deployed. However, even in the case of a file access, in a multiprogramming environment,
there will be I/O requests competing for the same disk. Thus, it is worthwhile
to examine ways in which the performance of disk I/O can be improved over
that achieved with purely random access to the disk. This leads to a consideration
of disk scheduling algorithms, which is the province of the operating system and
beyond the scope of this book (see [STAL18] for a discussion).

## Slide 13: Table 7.2 Typical Hard Disk Drive Parameters
Characteristics | HGST Ultrastar HE | HGST Ultrastar C15K600 | Toshiba L200
Application | Enterprise | Data Center | Laptop
Capacity | 12 TB | 600 GB | 500 GB
Average seek time | 8.0 ms read 8.6 ms write | 2.9 ms read 3.1 ms write | 11 ms
Spindle speed | 7200 rpm | 15,030 rpm | 5400 rpm
Average latency | 4.16 | < 2 ms | 5.6 ms
Maximum sustained transfer rate | 255 MB/s | 1.2 GB/s | 3 GB/s
Bytes per sector | 512/4096 | 512/4096 | 4096
Tracks per cylinder (number of platter surfaces) | 8 | 6 | 4
Cache | 256 MB | 128 MB | 16 MB
Diameter | 3.5 in (8.89 cm)s | 2.5 in (6.35 cm) | 2.5 in (6.35 cm)
Maximum areal density (Gb/cm2) | 134 | 82 | 66
Notes: Table 7.2 gives disk parameters for typical contemporary high-performance
disks. The HGST Ultrastar HE is intended for enterprise applications, such
as use in servers and workstations. The HGST Ultrastar C15K600 is designed for
use in high-performance computing and mission critical data center installations.
The Toshiba L200 is an internal laptop hard disk drive.
We can make some useful observations on this table. The seek time depends
in part on the power and quality of the arm actuator. On the other end of the spectrum,
a laptop disk needs to be small, inexpensive, and low power, so that the attainable
seek time is much greater. Seek time also depends on physical characteristics.
The Ultrastar C15K600 has a smaller diameter than the Ultrastar HE. With less
average distance to travel, the C15K600 achieves lower seek time. In addition, the
C15K600 has a lower bit density on the disk surface, so that less precision is needed
in positioning the read/write head, again contributing to lower seek time. Of course
the penalty of achieving these lower seek times is a much lower disk capacity. But
the Ultrastar C15K600 is likely to be used in applications that call for a high rate of
accesses to the disk, so it is reasonable to invest in minimizing the seek time.
Note that for the two HGST disks, the average seek time is less for reads than
for writes. For writes, more precision is required to place the write head dead center
on the track. Less precision is needed simply to sense the data that is already there.
For the block size, or bytes per physical sector, the two HGST disks can be
configured for 512 or 4096 bytes, and the laptop disk is offered only at 4096 bytes.
As discussed previously, the larger block size is more efficient in space and more
effective in error correction.

## Slide 14: RAID
Redundant Array of Independent Disks
Consists of 7 levels
Levels do not imply a hierarchical relationship but designate different design architectures that share three common characteristics:
  Set of physical disk drives viewed by the operating system as a single logical drive
  Data are distributed across the physical drives of an array in a scheme known as striping
  Redundant disk capacity is used to store parity information, which guarantees data recoverability in case of a disk failure
Notes: With the use of multiple disks, there is a wide variety of ways in which the data
can be organized and in which redundancy can be added to improve reliability. This
could make it difficult to develop database schemes that are usable on a number of
platforms and operating systems. Fortunately, industry has agreed on a standardized
scheme for multiple-disk database design, known as RAID (Redundant Array
of Independent Disks). The RAID scheme consists of seven levels, zero through six.
These levels do not imply a hierarchical relationship, but designate different
design architectures that share three common characteristics:
1. RAID is a set of physical disk drives viewed by the operating system as a single
logical drive.
2. Data are distributed across the physical drives of an array in a scheme known
as striping, described subsequently.
3. Redundant disk capacity is used to store parity information, which guarantees
data recoverability in case of a disk failure.
The details of the second and third characteristics differ for the different RAID
levels. RAID 0 and RAID 1 do not support the third characteristic.
The term RAID was originally coined in a paper by a group of researchers
at the University of California at Berkeley [PATT88]. The paper outlined various
RAID configurations and applications and introduced the definitions of the
RAID levels that are still used. The RAID strategy employs multiple disk drives
and distributes data in such a way as to enable simultaneous access to data from
multiple drives, thereby improving I/O performance and allowing easier incremental
increases in capacity.

## Slide 15: Table 7.3 RAID Levels
Category | Level | Description | Disks Required | Data Availability | Large I/O Data Transfer Capacity | Small I/O Request Rate
Striping | 0 | Nonredundant | N | Lower than single disk | Very high | Very high for both read and write
Mirroring | 1 | Mirrored | 2N | Higher than RAID 2, 3, 4, or 5; lower than RAID 6 | Higher than single disk for read; similar to single disk for write | Up to twice that of a single disk for read; similar to single disk for write
Parallel Access | 2 | Redundant via Hamming code | N + m | Much higher than single disk; comparable to RAID 3, 4, or 5 | Highest of all listed alternatives | Approximately twice that of a single disk
 | 3 | Bit-interleaved parity | N + 1 | Much higher than single disk; comparable to RAID 2, 4, or 5 | Highest of all listed alternatives | Approximately twice that of a single disk
Independent access | 4 | Block-interleaved parity | N + 1 | Much higher than single disk; comparable to RAID 2, 3, or 5 | Similar to RAID 0 for read; significantly lower than single disk for write | Similar to RAID 0 for read; significantly lower than single disk for write
 | 5 | Block-interleaved distributed parity | N + 1 | Much higher than single disk; comparable to RAID 2, 3, or 4 | Similar to RAID 0 for read; lower than single disk for write | Similar to RAID 0 for read; generally lower than single disk for write
 | 6 | Block-interleaved dual distributed parity | N + 2 | Highest of all listed alternatives | Similar to RAID 0 for read; lower than RAID 5 for write | Similar to RAID 0 for read; significantly lower than RAID 5 for write
N = number of data disks; m proportional to log N
Notes: The unique contribution of the RAID proposal is to address effectively the
need for redundancy. Although allowing multiple heads and actuators to operate
simultaneously achieves higher I/O and transfer rates, the use of multiple devices
increases the probability of failure. To compensate for this decreased reliability,
RAID makes use of stored parity information that enables the recovery of data lost
due to a disk failure.
We now examine each of the RAID levels. Table 7.3 provides a rough guide
to the seven levels. In the table, I/O performance is shown both in terms of data
transfer capacity, or ability to move data, and I/O request rate, or ability to satisfy
I/O requests, since these RAID levels inherently perform differently relative to
these two metrics. Each RAID level’s strong point is highlighted by darker shading.

## Slide 16: Figure 7.6 RAID Levels (1 of 2)
Notes: Figure 7.6 illustrates the use of the seven RAID schemes to support a data
capacity requiring four disks with no redundancy. The figures highlight the layout
of user data and redundant data and indicates the relative storage requirements of
the various levels. We refer to these figures throughout the following discussion.
Of the seven RAID levels described, only four are commonly used: RAID levels
0, 1, 5, and 6.

## Slide 17: Figure 7.6 RAID Levels (2 of 2)
Notes: Figure 7.6 continued.

## Slide 18: Figure 7.7 Data Mapping for a RAID Level 0 Array
Notes: RAID level 0 is not a true member of the RAID family because it does not include
redundancy to improve performance. However, there are a few applications, such as
some on supercomputers in which performance and capacity are primary concerns
and low cost is more important than improved reliability.
For RAID 0, the user and system data are distributed across all of the disks in
the array. This has a notable advantage over the use of a single large disk: If two-
different I/O requests are pending for two different blocks of data, then there is a
good chance that the requested blocks are on different disks. Thus, the two requests
can be issued in parallel, reducing the I/O queuing time.
But RAID 0, as with all of the RAID levels, goes further than simply distributing
the data across a disk array: The data are striped across the available disks. This
is best understood by considering Figure 7.7. All of the user and system data are
viewed as being stored on a logical disk. The logical disk is divided into strips; these
strips may be physical blocks, sectors, or some other unit. The strips are mapped
round robin to consecutive physical disks in the RAID array. A set of logically consecutive
strips that maps exactly one strip to each array member is referred to as a
stripe. In an n-disk array, the first n logical strips are physically stored as the first
strip on each of the n disks, forming the first stripe; the second n strips are distributed
as the second strips on each disk; and so on. The advantage of this layout is that if a
single I/O request consists of multiple logically contiguous strips, then up to n strips
for that request can be handled in parallel, greatly reducing the I/O transfer time.
Figure 7.7 indicates the use of array management software to map between
logical and physical disk space. This software may execute either in the disk subsystem
or in a host computer.

## Slide 19: RAID Level 0
RAID 0 for High Data Transfer Capacity
For applications to experience a high transfer rate two requirements must be met:
  A high transfer capacity must exist along the entire path between host memory and the individual disk drives
  The application must make I/O requests that drive the disk array efficiently
RAID 0 for High I/O Request Rate
Addresses the issues of request patterns of the host system and layout of the data
Impact of redundancy does not interfere with analysis
For an individual I/O request for a small amount of data the I/O time is dominated by the seek time and rotational latency
A disk array can provide high I/O execution rates by balancing the I/O load across multiple disks
If the strip size is relatively large multiple waiting I/O requests can be handled in parallel, reducing the queuing time for each request
Notes: The performance of any of the
RAID levels depends critically on the request patterns of the host system and on
the layout of the data. These issues can be most clearly addressed in RAID 0, where
the impact of redundancy does not interfere with the analysis. First, let us consider
the use of RAID 0 to achieve a high data transfer rate. For applications to experience
a high transfer rate, two requirements must be met. First, a high transfer capacity
must exist along the entire path between host memory and the individual disk drives.
This includes internal controller buses, host system I/O buses, I/O adapters, and host
memory buses.
The second requirement is that the application must make I/O requests that
drive the disk array efficiently. This requirement is met if the typical request is for
large amounts of logically contiguous data, compared to the size of a strip. In this
case, a single I/O request involves the parallel transfer of data from multiple disks,
increasing the effective transfer rate compared to a single-disk transfer.
In a transaction-oriented environment, the user is typically more concerned with
response time than with transfer rate. For
an individual I/O request for a small amount of data, the I/O time is dominated by the
motion of the disk heads (seek time) and the movement of the disk (rotational latency).
In a transaction environment, there may be hundreds of I/O requests per second.
A disk array can provide high I/O execution rates by balancing the I/O load
across multiple disks. Effective load balancing is achieved only if there are typically
multiple I/O requests outstanding. This, in turn, implies that there are multiple independent
applications or a single transaction-oriented application that is capable of
multiple asynchronous I/O requests. The performance will also be influenced by the
strip size. If the strip size is relatively large, so that a single I/O request only involves
a single disk access, then multiple waiting I/O requests can be handled in parallel,
reducing the queuing time for each request.

## Slide 20: RAID Level 1
Characteristics
Differs from RAID levels 2 through 6 in the way in which redundancy is achieved
Redundancy is achieved by the simple expedient of duplicating all the data
Data striping is used but each logical strip is mapped to two separate physical disks so that every disk in the array has a mirror disk that contains the same data
RAID 1 can also be implemented without data striping, although this is less common
Positive Aspects
A read request can be serviced by either of the two disks that contains the requested data
There is no “write penalty”
Recovery from a failure is simple, when a drive fails the data can be accessed from the second drive
Provides real-time copy of all data
Can achieve high I/O request rates if the bulk of the requests are reads
Principal disadvantage is the cost
Notes: The performance of any of the
RAID levels depends critically on the request patterns of the host system and on
the layout of the data. These issues can be most clearly addressed in RAID 0, where
the impact of redundancy does not interfere with the analysis. First, let us consider
the use of RAID 0 to achieve a high data transfer rate. For applications to experience
a high transfer rate, two requirements must be met. First, a high transfer capacity
must exist along the entire path between host memory and the individual disk drives.
This includes internal controller buses, host system I/O buses, I/O adapters, and host
memory buses.
The second requirement is that the application must make I/O requests that
drive the disk array efficiently. This requirement is met if the typical request is for
large amounts of logically contiguous data, compared to the size of a strip. In this
case, a single I/O request involves the parallel transfer of data from multiple disks,
increasing the effective transfer rate compared to a single-disk transfer.
In a transaction-oriented environment, the user is typically more concerned with
response time than with transfer rate. For
an individual I/O request for a small amount of data, the I/O time is dominated by the
motion of the disk heads (seek time) and the movement of the disk (rotational latency).
In a transaction environment, there may be hundreds of I/O requests per second.
A disk array can provide high I/O execution rates by balancing the I/O load
across multiple disks. Effective load balancing is achieved only if there are typically
multiple I/O requests outstanding. This, in turn, implies that there are multiple independent
applications or a single transaction-oriented application that is capable of
multiple asynchronous I/O requests. The performance will also be influenced by the
strip size. If the strip size is relatively large, so that a single I/O request only involves
a single disk access, then multiple waiting I/O requests can be handled in parallel,
reducing the queuing time for each request.

## Slide 21: RAID Level 2
Characteristics
Makes use of a parallel access technique
In a parallel access array all member disks participate in the execution of every I/O request
Spindles of the individual drives are synchronized so that each disk head is in the same position on each disk at any given time
Data striping is used
Strips are very small, often as small as a single byte or word
Performance
An error-correcting code is calculated across corresponding bits on each data disk and the bits of the code are stored in the corresponding bit positions on multiple parity disks
Typically a Hamming code is used, which is able to correct single-bit errors and detect double-bit errors
The number of redundant disks is proportional to the log of the number of data disks
Would only be an effective choice in an environment in which many disk errors occur
Notes: The performance of any of the
RAID levels depends critically on the request patterns of the host system and on
the layout of the data. These issues can be most clearly addressed in RAID 0, where
the impact of redundancy does not interfere with the analysis. First, let us consider
the use of RAID 0 to achieve a high data transfer rate. For applications to experience
a high transfer rate, two requirements must be met. First, a high transfer capacity
must exist along the entire path between host memory and the individual disk drives.
This includes internal controller buses, host system I/O buses, I/O adapters, and host
memory buses.
The second requirement is that the application must make I/O requests that
drive the disk array efficiently. This requirement is met if the typical request is for
large amounts of logically contiguous data, compared to the size of a strip. In this
case, a single I/O request involves the parallel transfer of data from multiple disks,
increasing the effective transfer rate compared to a single-disk transfer.
In a transaction-oriented environment, the user is typically more concerned with
response time than with transfer rate. For
an individual I/O request for a small amount of data, the I/O time is dominated by the
motion of the disk heads (seek time) and the movement of the disk (rotational latency).
In a transaction environment, there may be hundreds of I/O requests per second.
A disk array can provide high I/O execution rates by balancing the I/O load
across multiple disks. Effective load balancing is achieved only if there are typically
multiple I/O requests outstanding. This, in turn, implies that there are multiple independent
applications or a single transaction-oriented application that is capable of
multiple asynchronous I/O requests. The performance will also be influenced by the
strip size. If the strip size is relatively large, so that a single I/O request only involves
a single disk access, then multiple waiting I/O requests can be handled in parallel,
reducing the queuing time for each request.

## Slide 22: RAID Level 3
Redundancy
Requires only a single redundant disk, no matter how large the disk array
Employs parallel access, with data distributed in small strips
Instead of an error correcting code, a simple parity bit is computed for the set of individual bits in the same position on all of the data disks
Can achieve very high data transfer rates
Performance
In the event of a drive failure, the parity drive is accessed and data is reconstructed from the remaining devices
Once the failed drive is replaced, the missing data can be restored on the new drive and operation resumed
In the event of a disk failure, all of the data are still available in what is referred to as reduced mode
Return to full operation requires that the failed disk be replaced and the entire contents of the failed disk be regenerated on the new disk
In a transaction-oriented environment performance suffers
Notes: The performance of any of the
RAID levels depends critically on the request patterns of the host system and on
the layout of the data. These issues can be most clearly addressed in RAID 0, where
the impact of redundancy does not interfere with the analysis. First, let us consider
the use of RAID 0 to achieve a high data transfer rate. For applications to experience
a high transfer rate, two requirements must be met. First, a high transfer capacity
must exist along the entire path between host memory and the individual disk drives.
This includes internal controller buses, host system I/O buses, I/O adapters, and host
memory buses.
The second requirement is that the application must make I/O requests that
drive the disk array efficiently. This requirement is met if the typical request is for
large amounts of logically contiguous data, compared to the size of a strip. In this
case, a single I/O request involves the parallel transfer of data from multiple disks,
increasing the effective transfer rate compared to a single-disk transfer.
In a transaction-oriented environment, the user is typically more concerned with
response time than with transfer rate. For
an individual I/O request for a small amount of data, the I/O time is dominated by the
motion of the disk heads (seek time) and the movement of the disk (rotational latency).
In a transaction environment, there may be hundreds of I/O requests per second.
A disk array can provide high I/O execution rates by balancing the I/O load
across multiple disks. Effective load balancing is achieved only if there are typically
multiple I/O requests outstanding. This, in turn, implies that there are multiple independent
applications or a single transaction-oriented application that is capable of
multiple asynchronous I/O requests. The performance will also be influenced by the
strip size. If the strip size is relatively large, so that a single I/O request only involves
a single disk access, then multiple waiting I/O requests can be handled in parallel,
reducing the queuing time for each request.

## Slide 23: RAID Level 4
Characteristics
Makes use of an independent access technique
  In an independent access array, each member disk operates independently so that separate I/O requests can be satisfied in parallel
Data striping is used
          Strips are relatively large
To calculate the new parity the array management software must read the old user strip and the old parity strip
Performance
Involves a write penalty when an I/O write request of small size is performed
Each time a write occurs the array management software must update not only the user data but also the corresponding parity bits
Thus each strip write involves two reads and two writes
Notes: The performance of any of the
RAID levels depends critically on the request patterns of the host system and on
the layout of the data. These issues can be most clearly addressed in RAID 0, where
the impact of redundancy does not interfere with the analysis. First, let us consider
the use of RAID 0 to achieve a high data transfer rate. For applications to experience
a high transfer rate, two requirements must be met. First, a high transfer capacity
must exist along the entire path between host memory and the individual disk drives.
This includes internal controller buses, host system I/O buses, I/O adapters, and host
memory buses.
The second requirement is that the application must make I/O requests that
drive the disk array efficiently. This requirement is met if the typical request is for
large amounts of logically contiguous data, compared to the size of a strip. In this
case, a single I/O request involves the parallel transfer of data from multiple disks,
increasing the effective transfer rate compared to a single-disk transfer.
In a transaction-oriented environment, the user is typically more concerned with
response time than with transfer rate. For
an individual I/O request for a small amount of data, the I/O time is dominated by the
motion of the disk heads (seek time) and the movement of the disk (rotational latency).
In a transaction environment, there may be hundreds of I/O requests per second.
A disk array can provide high I/O execution rates by balancing the I/O load
across multiple disks. Effective load balancing is achieved only if there are typically
multiple I/O requests outstanding. This, in turn, implies that there are multiple independent
applications or a single transaction-oriented application that is capable of
multiple asynchronous I/O requests. The performance will also be influenced by the
strip size. If the strip size is relatively large, so that a single I/O request only involves
a single disk access, then multiple waiting I/O requests can be handled in parallel,
reducing the queuing time for each request.

## Slide 24: RAID Level 5
Characteristics
Organized in a similar fashion to RAID 4
Difference is distribution of the parity strips across all disks
A typical allocation is a round-robin scheme
The distribution of parity strips across all drives avoids the potential I/O bottleneck found in RAID 4
RAID Level 6
Characteristics
Two different parity calculations are carried out and stored in separate blocks on different disks
Advantage is that it provides extremely high data availability
Three disks would have to fail within the mean time to repair (MTTR) interval to cause data to be lost
Incurs a substantial write penalty because each write affects two parity blocks
Notes: The performance of any of the
RAID levels depends critically on the request patterns of the host system and on
the layout of the data. These issues can be most clearly addressed in RAID 0, where
the impact of redundancy does not interfere with the analysis. First, let us consider
the use of RAID 0 to achieve a high data transfer rate. For applications to experience
a high transfer rate, two requirements must be met. First, a high transfer capacity
must exist along the entire path between host memory and the individual disk drives.
This includes internal controller buses, host system I/O buses, I/O adapters, and host
memory buses.
The second requirement is that the application must make I/O requests that
drive the disk array efficiently. This requirement is met if the typical request is for
large amounts of logically contiguous data, compared to the size of a strip. In this
case, a single I/O request involves the parallel transfer of data from multiple disks,
increasing the effective transfer rate compared to a single-disk transfer.
In a transaction-oriented environment, the user is typically more concerned with
response time than with transfer rate. For
an individual I/O request for a small amount of data, the I/O time is dominated by the
motion of the disk heads (seek time) and the movement of the disk (rotational latency).
In a transaction environment, there may be hundreds of I/O requests per second.
A disk array can provide high I/O execution rates by balancing the I/O load
across multiple disks. Effective load balancing is achieved only if there are typically
multiple I/O requests outstanding. This, in turn, implies that there are multiple independent
applications or a single transaction-oriented application that is capable of
multiple asynchronous I/O requests. The performance will also be influenced by the
strip size. If the strip size is relatively large, so that a single I/O request only involves
a single disk access, then multiple waiting I/O requests can be handled in parallel,
reducing the queuing time for each request.

## Slide 25: Table 7.4 RAID Comparison (1 of 2)
Level | Advantages | Disadvantages | Applications
0 | I/O performance is greatly improved by spreading the I/O load across many channels and drives No parity calculation overhead is involved Very simple design Easy to implement | The failure of just one drive will result in all data in an array being lost | Video production and editing Image Editing Pre- press applications Any application requiring high bandwidth
1 | 100% redundancy of data means no rebuild is necessary in case of a disk failure, just a copy to the replacement disk Under certain circumstances, RAID 1 can sustain multiple simultaneous drive Failures Simplest RAID storage subsystem design | Highest disk overhead of all RAID types (100%)—inefficient | Accounting Payroll Financial Any application requiring very high availability
2 | Extremely high data transfer rates possible The higher the data transfer rate required, the better the ratio of data disks to ECC disks Relatively simple controller design compared to RAID levels 3, 4, & 5 | Very high ratio of ECC disks to data disks with smaller word sizes— inefficient Entry level cost very high— requires very high transfer rate requirement to justify | No commercial imple-mentations exist/not commercially viable
3 | Very high read data transfer rate Very high write data transfer rate Disk failure has an insignificant impact on throughput Low ratio of ECC (parity) disks to data disks means high efficiency | Transaction rate equal to that of a single disk drive at best (if spindles are synchronized) Controller design is fairly complex | Video production and live streaming Image editing Video editing Prepress applications Any application requiring high throughput
(Table can be found
on pages 230-231 in
the textbook.)
Notes: Table 7.4 is a comparative summary of the seven levels.

## Slide 26: Table 7.4 RAID Comparison (2 of 2)
Level | Advantages | Disadvantages | Applications
4 | Very high Read data transaction rate Low ratio of ECC (parity) disks to data disks means high efficiency | Quite complex controller design Worst write transaction rate and Write aggregate transfer rate Difficult and inefficient data rebuild in the event of disk failure | No commercial implementations exist/not commercially viable
5 | Highest Read data transaction rate Low ratio of ECC (parity) disks to data disks means high efficiency Good aggregate transfer rate | Most complex controller design Difficult to rebuild in the event of a disk failure (as compared to RAID level 1) | File and application servers Database servers Web, e- mail, and news servers Intranet servers Most versatile RAID level
6 | Provides for an extremely high data fault tolerance and can sustain multiple simultaneous drive failures | More complex controller design Controller overhead to compute parity addresses is extremely high | Perfect solution for mission critical applications
(Table can be found on
pages 230-231 in the textbook.)
Notes: Table 7.4 RAID comparison (page 2 of 2)

## Slide 27: SSD Compared to HDD
SSDs have the following advantages over HDDs:
  High-performance input/output operations per second (IOPS)
  Durability
  Longer lifespan
  Lower power consumption
  Quieter and cooler running capabilities
  Lower access times and latency rates
Notes: One of the most significant developments in computer architecture in recent years is
the increasing use of solid state drives (SSDs) to complement or even replace hard
disk drives (HDDs) , both as internal and external secondary memory. The term solid
state refers to electronic circuitry built with semiconductors. An SSD is a memory
device made with solid state components that can be used as a replacement to a
hard disk drive. The SSDs now on the market and coming on line use NAND flash
memory, which is described in Chapter 5.
SSDs have the following advantages over HDDs:
• High-performance input/output operations per second (IOPS): Significantly
increases performance I/O subsystems.
• Durability: Less susceptible to physical shock and vibration.
• Longer lifespan: SSDs are not susceptible to mechanical wear.
• Lower power consumption: SSDs use considerably less than comparable-size HDDs.
• Quieter and cooler running capabilities: Less floor space required, lower
energy costs, and a greener enterprise.
• Lower access times and latency rates: Over 10 times faster than the spinning
disks in an HDD.
Currently, HDDs enjoy a cost per bit advantage and a capacity advantage, but
these differences are shrinking.

## Slide 28: Table 7.5 Comparison of Solid State Drives and Disk Drives
 | NAND Flash Drives | Seagate Laptop Internal HDD
File copy/write speed | 200–550 Mbps | 50–120 Mbps
Power draw/battery life | Less power draw, averages 2–3 watts, resulting in 30+ minute battery boost | More power draw, averages 6–7 watts and therefore uses more battery
Storage capacity | Typically not larger than 1 TB for Notebook size drives; 4 max for desktops | Typically around 500 GB and 2 TB max for notebook size drives; 10 TB max for desktops
Cost | Approx. $0.20 per GB for a 1-TB drive | Approx. $0.03 per GB for a 4-TB drive
Notes: As the cost of flash-based SSDs has dropped and the performance and bit density
increased, SSDs have become increasingly competitive with HDDs. Table 7.5 shows
typical measures of comparison at the time of this writing.

## Slide 29: Figure 7.8 Solid State Drive Architecture
Notes: Figure 7.8 illustrates a general view of the common architectural system component
associated with any SSD system. On the host system, to operating system invokes
file system software to access data on the disk. The file system, in turn, invokes I/O
driver software. The I/O driver software provides host access to the particular SSD
product. The interface component in Figure 7.8 refers to the physical and electrical
interface between the host processor and the SSD peripheral device. If the device is
an internal hard drive, a common interface is PCIe. For external devices, one common
interface is USB.
In addition to the interface to the host system, the SSD contains the following
components:
• Controller: Provides SSD device level interfacing and firmware execution.
• Addressing: Logic that performs the selection function across the flash
memory components.
• Data buffer/cache: High speed RAM memory components used for speed
matching and to increased data throughput.
• Error correction: Logic for error detection and correction.
• Flash memory components: Individual NAND flash chips.

## Slide 30: Practical Issues
There are two practical issues peculiar to SSDs that are not faced by HDDs:
SDD performance has a tendency to slow down as the device is used
  The entire block must be read from the flash memory and placed in a RAM buffer
  Before the block can be written back to flash memory, the entire block of flash memory must be erased
  The entire block from the buffer is now written back to the flash memory
Flash memory becomes unusable after a certain number of writes
  Techniques for prolonging life:
    Front-ending the flash with a cache to delay and group write operations
    Using wear-leveling algorithms that evenly distribute writes across block of cells
    Bad-block management techniques
  Most flash devices estimate their own remaining lifetimes so systems can anticipate failure and take preemptive action
Notes: There are two practical issues peculiar to SSDs that are not faced by HDDs. First,
SDD performance has a tendency to slow down as the device is used. To understand
the reason for this, you need to know that files are stored on disk as a set of pages,
typically 4 KB in length. These pages are not necessarily, and indeed not typically,
stored as a contiguous set of pages on the disk. The reason for this arrangement is
explained in our discussion of virtual memory in Chapter 9. However, flash memory
is accessed in blocks, with a typically block size of 512 KB, so that there are typically
128 pages per block. Now consider what must be done to write a page onto a flash
memory.
1. The entire block must be read from the flash memory and placed in a RAM
buffer. Then the appropriate page in the RAM buffer is updated.
2. Before the block can be written back to flash memory, the entire block of flash
memory must be erased—it is not possible to erase just one page of the flash
memory.
3. The entire block from the buffer is now written back to the flash memory.
Now, when a flash drive is relatively empty and a new file is created, the
pages of that file are written on to the drive contiguously, so that one or only a few
blocks are affected. However, over time, because of the way virtual memory works,
files become fragmented, with pages scattered over multiple blocks. As the drive
become more occupied, there is more fragmentation, so the writing of a new file can
affect multiple blocks. Thus, the writing of multiple pages from one block becomes
slower, the more fully occupied the disk is. Manufacturers have developed a variety
of techniques to compensate for this property of flash memory, such as setting aside
a substantial portion of the SSD as extra space for write operations (called over provisioning),
then to erase inactive pages during idle time used to defragment the
disk. Another technique is the TRIM command, which allows an operating system
to inform a solid state drive (SSD) which blocks of data are no longer considered in
use and can be wiped internally.
A second practical issue with flash memory drives is that a flash memory
becomes unusable after a certain number of writes. As flash cells are stressed,
they lose their ability to record and retain values. A typical limit is 100,000 writes
[GSOE08]. Techniques for prolonging the life of an SSD drive include front-ending
the flash with a cache to delay and group write operations, using wear-leveling algorithms
that evenly distribute writes across block of cells, and sophisticated bad-block
management techniques. In addition, vendors are deploying SSDs in RAID configurations
to further reduce the probability of data loss. Most flash devices are also
capable of estimating their own remaining lifetimes so systems can anticipate failure
and take preemptive action.

## Slide 31: Table 7.6 Optical Disk Products
CD Compact Disk. A nonerasable disk that stores digitized audio information. The standard system uses 12-cm disks and can record more than 60 minutes of uninterrupted playing time. CD-ROM Compact Disk Read- Only Memory. A nonerasable disk used for storing computer data. The standard system uses 12-cm disks and can hold more than 650 Mbytes. CD-R CD Recordable. Similar to a CD-ROM. The user can write to the disk only once. CD-RW CD Rewritable. Similar to a CD-ROM. The user can erase and rewrite to the disk multiple times. DVD Digital Versatile Disk. A technology for producing digitized, compressed representation of video information, as well as large volumes of other digital data. Both 8 and 12 cm diameters are used, with a double-sided capacity of up to 17 Gbytes. The basic DVD is read-only (DVD-ROM). DVD-R DVD Recordable. Similar to a DVD-ROM. The user can write to the disk only once. Only one-sided disks can be used. DVD-RW DVD Rewritable. Similar to a DVD-ROM. The user can erase and rewrite to the disk multiple times. Only one- sided disks can be used. Blu-ray DVD High-definition video disk. Provides considerably greater data storage density than DVD, using a 405-nm (blue- violet) laser. A single layer on a single side can store 25 Gbytes.
Notes: In 1983, one of the most successful consumer products of all time was introduced:
the compact disk (CD) digital audio system. The CD is a non-erasable disk that can
store more than 60 minutes of audio information on one side. The huge commercial
success of the CD enabled the development of low-cost optical-disk storage
technology that has revolutionized computer data storage. A variety of optical-disk
systems have been introduced (Table 7.6). We briefly review each of these.

## Slide 32: Compact Disk Read-Only Memory (CD-ROM)
Audio CD and the CD-ROM share a similar technology
  The main difference is that CD-ROM players are more rugged and have error correction devices to ensure that data are properly transferred
  Production:
  The disk is formed from a resin such as polycarbonate
  Digitally recorded information is imprinted as a series of microscopic pits on the surface of the polycarbonate
    This is done with a finely focused, high intensity laser to create a master disk
  The master is used, in turn, to make a die to stamp out copies onto polycarbonate
  The pitted surface is then coated with a highly reflective surface, usually aluminum or gold
  This shiny surface is protected against dust and scratches by a top coat of clear acrylic
  Finally a label can be silkscreened onto the acrylic
Notes: Both the audio CD and the CD-ROM (compact disk read-only
memory) share a similar technology. The main difference is that CD-ROM players
are more rugged and have error correction devices to ensure that data are properly
transferred from disk to computer. Both types of disk are made the same way. The
disk is formed from a resin, such as polycarbonate. Digitally recorded information
(either music or computer data) is imprinted as a series of microscopic pits on the
surface of the polycarbonate. This is done, first of all, with a finely focused, high intensity
laser to create a master disk. The master is used, in turn, to make a die to
stamp out copies onto polycarbonate. The pitted surface is then coated with a highly
reflective surface, usually aluminum or gold. This shiny surface is protected against
dust and scratches by a top coat of clear acrylic. Finally, a label can be silkscreened
onto the acrylic.

## Slide 33: Figure 7.9 CD Operation
Notes: Information is retrieved from a CD or CD-ROM by a low-powered laser
housed in an optical-disk player, or drive unit. The laser shines through the clear
polycarbonate while a motor spins the disk past it (Figure 7.9). The intensity of
the reflected light of the laser changes as it encounters a pit. Specifically, if the laser
beam falls on a pit, which has a somewhat rough surface, the light scatters and a low
intensity is reflected back to the source. The areas between pits are called lands.
A land is a smooth surface, which reflects back at higher intensity. The change
between pits and lands is detected by a photo sensor and converted into a digital
signal. The sensor tests the surface at regular intervals. The beginning or end of
a pit represents a 1; when no change in elevation occurs between intervals, a 0 is
recorded.
Recall that on a magnetic disk, information is recorded in concentric tracks.
With the simplest constant angular velocity (CAV) system, the number of bits per
track is constant. An increase in density is achieved with multiple zoned recording,
in which the surface is divided into a number of zones, with zones farther from the
center containing more bits than zones closer to the center. Although this technique
increases capacity, it is still not optimal.
To achieve greater capacity, CDs and CD-ROMs do not organize information
on concentric tracks. Instead, the disk contains a single spiral track, beginning near
the center and spiraling out to the outer edge of the disk. Sectors near the outside
of the disk are the same length as those near the inside. Thus, information is packed
evenly across the disk in segments of the same size and these are scanned at the
same rate by rotating the disk at a variable speed. The pits are then read by the laser
at a constant linear velocity (CLV). The disk rotates more slowly for accesses near
the outer edge than for those near the center. Thus, the capacity of a track and the
rotational delay both increase for positions nearer the outer edge of the disk. The
data capacity for a CD-ROM is about 680 MB.

## Slide 34: Figure 7.10 CD-ROM Block Format
Notes: Data on the CD-ROM are organized as a sequence of blocks. A typical block
format is shown in Figure 7.10. It consists of the following fields:
• Sync: The sync field identifies the beginning of a block. It consists of a byte of
all 0s, 10 bytes of all 1s, and a byte of all 0s.
• Header: The header contains the block address and the mode byte. Mode
0 specifies a blank data field; mode 1 specifies the use of an error-correcting
code and 2048 bytes of data; mode 2 specifies 2336 bytes of user data with no
error-correcting code.
• Data: User data.
• Auxiliary: Additional user data in mode 2. In mode 1, this is a 288-byte error correcting
code.
With the use of CLV, random access becomes more difficult. Locating a specific
address involves moving the head to the general area, adjusting the rotation
speed and reading the address, and then making minor adjustments to find and
access the specific sector.

## Slide 35: CD-ROM
CD-ROM is appropriate for the distribution of large amounts of data to a large number of users
Because the expense of the initial writing process it is not appropriate for individualized applications
The CD-ROM has two advantages:
    The optical disk together with the information stored on it can be mass replicated inexpensively
    The optical disk is removable, allowing the disk itself to be used for archival storage
  The CD-ROM disadvantages:
    It is read-only and cannot be updated
    It has an access time much longer than that of a magnetic disk drive
Notes: CD-ROM is appropriate for the distribution of large amounts of data to a
large number of users. Because of the expense of the initial writing process, it is not
appropriate for individualized applications. Compared with traditional magnetic
disks, the CD-ROM has two advantages:
• The optical disk together with the information stored on it can be mass replicated
inexpensively—unlike a magnetic disk. The database on a magnetic disk
has to be reproduced by copying one disk at a time using two disk drives.
• The optical disk is removable, allowing the disk itself to be used for archival
storage. Most magnetic disks are non-removable. The information on non-removable
magnetic disks must first be copied to another storage medium
before the disk drive/disk can be used to store new information.
The disadvantages of CD-ROM are as follows:
• It is read-only and cannot be updated.
• It has an access time much longer than that of a magnetic disk drive, as much
as half a second.

## Slide 36: CD Recordable CD Rewritable (CD-R) (CD-RW)
Write-once read-many
Accommodates applications in which only one or a small number of copies of a set of data is needed
Disk is prepared in such a way that it can be subsequently written once with a laser beam of modest-intensity
Medium includes a dye layer which is used to change reflectivity and is activated by a high-intensity laser
Provides a permanent record of large volumes of user data
Can be repeatedly written and overwritten
Phase change disk uses a material that has two significantly different reflectivities in two different phase states
Amorphous state
  Molecules exhibit a random orientation that reflects light poorly
Crystalline state
  Has a smooth surface that reflects light well
A beam of laser light can change the material from one phase to the other
Disadvantage is that the material eventually and permanently loses its desirable properties
Advantage is that it can be rewritten
Notes: To accommodate applications in which only one or a small
number of copies of a set of data is needed, the write-once read-many CD, known
as the CD recordable (CD-R), has been developed. For CD-R, a disk is prepared
in such a way that it can be subsequently written once with a laser beam of
modest -intensity. Thus, with a some what more expensive disk controller than for
CD-ROM, the customer can write once as well as read the disk.
The CD-R medium is similar to but not identical to that of a CD or
CD-ROM. For CDs and CD-ROMs, information is recorded by the pitting of
the surface of the medium, which changes reflectivity. For a CD-R, the medium
includes a dye layer. The dye is used to change reflectivity and is activated
by a high-intensity laser. The resulting disk can be read on a CD-R drive or a
CD-ROM drive.
The CD-R optical disk is attractive for archival storage of documents and files.
It provides a permanent record of large volumes of user data.
The CD-RW optical disk can be repeatedly written and
overwritten, as with a magnetic disk. Although a number of approaches have been
tried, the only pure optical approach that has proved attractive is called phase
change. The phase change disk uses a material that has two significantly different
reflectivities in two different phase states. There is an amorphous state, in which the
molecules exhibit a random orientation that reflects light poorly; and a crystalline
state, which has a smooth surface that reflects light well. A beam of laser light can
change the material from one phase to the other. The primary disadvantage of
phase change optical disks is that the material eventually and permanently loses
its desirable properties. Current materials can be used for between 500,000 and
1,000,000 erase cycles.
The CD-RW has the obvious advantage over CD-ROM and CD-R that it can
be rewritten and thus used as a true secondary storage. As such, it competes with
magnetic disk. A key advantage of the optical disk is that the engineering tolerances
for optical disks are much less severe than for high-capacity magnetic disks. Thus,
they exhibit higher reliability and longer life.

## Slide 37: Figure 7.11 CD-ROM and DVD-ROM
Notes: With the capacious digital versatile disk (DVD), the electronics industry has at last
found an acceptable replacement for the analog VHS video tape. The DVD has
replaced the videotape used in video cassette recorders (VCRs) and, more important
for this discussion, replace the CD-ROM in personal computers and servers.
The DVD takes video into the digital age. It delivers movies with impressive picture
quality, and it can be randomly accessed like audio CDs, which DVD machines
can also play. Vast volumes of data can be crammed onto the disk, currently seven
times as much as a CD-ROM. With DVD’s huge storage capacity and vivid quality,
PC games have become more realistic and educational software incorporates more
video. Following in the wake of these developments has been a new crest of traffic
over the Internet and corporate intranets, as this material is incorporated into
Web sites.
The DVD’s greater capacity is due to three differences from CDs (Figure 7.11):
1. Bits are packed more closely on a DVD. The spacing between loops of a spiral on a
CD is 1.6 μm and the minimum distance between pits along the spiral is 0.834 μm.
The DVD uses a laser with shorter wavelength and achieves a loop spacing of
0.74 μm and a minimum distance between pits of 0.4 μm. The result of these
two improvements is about a seven-fold increase in capacity, to about 4.7 GB.
2. The DVD employs a second layer of pits and lands on top of the first layer. A
dual-layer DVD has a semi-reflective layer on top of the reflective layer, and
by adjusting focus, the lasers in DVD drives can read each layer separately.
This technique almost doubles the capacity of the disk, to about 8.5 GB. The
lower reflectivity of the second layer limits its storage capacity so that a full
doubling is not achieved.
3. The DVD-ROM can be two sided, whereas data are recorded on only one side
of a CD. This brings total capacity up to 17 GB.
As with the CD, DVDs come in writeable as well as read-only versions (Table 7.6).

## Slide 38: Figure 7.12 Optical Memory Characteristics
Notes: High-definition optical disks are designed to store high-definition videos and to
provide significantly greater storage capacity compared to DVDs. The higher bit
density is achieved by using a laser with a shorter wavelength, in the blue-violet
range. The data pits, which constitute the digital 1s and 0s, are smaller on the high-definition
optical disks compared to DVD because of the shorter laser wavelength.
Two competing disk formats and technologies initially competed for market
acceptance: HD DVD and Blu-ray DVD. The Blu-ray scheme ultimately achieved
market dominance. The HD DVD scheme can store 15 GB on a single layer on a
single side. Blu-ray positions the data layer on the disk closer to the laser (shown on
the right-hand side of each diagram in Figure 7.12). This enables a tighter focus and
less distortion and thus smaller pits and tracks. Blu-ray can store 25 GB on a single
layer. Three versions are available: read only (BD-ROM), recordable once (BD-R),
and re-recordable (BD-RE).

## Slide 39: Magnetic Tape
Tape systems use the same reading and recording techniques as disk systems
Medium is flexible polyester tape coated with magnetizable material
Coating may consist of particles of pure metal in special binders or vapor-plated metal films
Data on the tape are structured as a number of parallel tracks running lengthwise
Serial recording
  Data are laid out as a sequence of bits along each track
  Data are read and written in contiguous blocks called physical records
  Blocks on the tape are separated by gaps referred to as inter-record gaps
Notes: Tape systems use the same reading and recording techniques as disk systems. The
medium is flexible polyester (similar to that used in some clothing) tape coated with
magnetizable material. The coating may consist of particles of pure metal in special
binders or vapor-plated metal films. The tape and the tape drive are analogous
to a home tape recorder system. Tape widths vary from 0.38 cm (0.15 inch) to
1.27 cm (0.5 inch). Tapes used to be packaged as open reels that have to be threaded
through a second spindle for use. Today, virtually all tapes are housed in cartridges.
Data on the tape are structured as a number of parallel tracks running lengthwise.
Earlier tape systems typically used nine tracks. This made it possible to store
data one byte at a time, with an additional parity bit as the ninth track. This was
followed by tape systems using 18 or 36 tracks, corresponding to a digital word or
double word. The recording of data in this form is referred to as parallel recording.
Most modern systems instead use serial recording, in which data are laid out as a
sequence of bits along each track, as is done with magnetic disks. As with the disk,
data are read and written in contiguous blocks, called physical records, on a tape.
Blocks on the tape are separated by gaps referred to as inter-record gaps. As with the
disk, the tape is formatted to assist in locating physical records.

## Slide 40: Figure 7.13 Typical Magnetic Tape Features
Notes: The typical recording technique used in serial tapes is referred to as serpentine
recording. In this technique, when data are being recorded, the first set of bits is
recorded along the whole length of the tape. When the end of the tape is reached,
the heads are repositioned to record a new track, and the tape is again recorded on
its whole length, this time in the opposite direction. That process continues, back
and forth, until the tape is full (Figure 7.13a). To increase speed, the read-write
head is capable of reading and writing a number of adjacent tracks simultaneously
(typically two to eight tracks). Data are still recorded serially along individual tracks,
but blocks in sequence are stored on adjacent tracks, as suggested by Figure 7.13b.
A tape drive is a sequential-access device. If the tape head is positioned at
record 1, then to read record N, it is necessary to read physical records 1 through
N - 1, one at a time. If the head is currently positioned beyond the desired record, it
is necessary to rewind the tape a certain distance and begin reading forward. Unlike
the disk, the tape is in motion only during a read or write operation.
In contrast to the tape, the disk drive is referred to as a direct-access device. A
disk drive need not read all the sectors on a disk sequentially to get to the desired
one. It must only wait for the intervening sectors within one track and can make successive
accesses to any track.
Magnetic tape was the first kind of secondary memory. It is still widely used as
the lowest-cost, slowest-speed member of the memory hierarchy.

## Slide 41: Table 7.7 LTO Tape Drives
 | LTO-1 | LTO-2 | LTO-3 | LTO-4 | LTO-5 | LTO-6 | LTO-7 | LTO-8
Release date | 2000 | 2003 | 2005 | 2007 | 2010 | 2012 | TBA | TBA
Compressed capacity | 200 GB | 400 GB | 800 GB | 1600 GB | 3.2 TB | 8 TB | 16 TB | 32 TB
Compressed transfer rate | 40 MB/s | 80 MB/s | 160 MB/s | 240 MB/s | 280 MB/s | 400 MB/s | 788 MB/s | 1.18 GB/s
Linear density (bits/mm) | 4880 | 7398 | 9638 | 13,250 | 15,142 | 15,143 | 19,094 | 
Tape tracks | 384 | 512 | 704 | 896 | 1280 | 2176 | 3,584 | 
Tape length (m) | 609 | 609 | 680 | 820 | 846 | 846 | 960 | 
Tape width (cm) | 1.27 | 1.27 | 1.27 | 1.27 | 1.27 | 1.27 | 1.27 | 
Write elements | 8 | 8 | 16 | 16 | 16 | 16 | 32 | 
WORM? | No | No | Yes | Yes | Yes | Yes | Yes | Yes
Encryption Capable? | No | No | No | Yes | Yes | Yes | Yes | Yes
Partitioning? | No | No | No | No | Yes | Yes | Yes | Yes
(Table can be found on page 241 in the textbook.)
Notes: The dominant tape technology today is a cartridge system known as linear
tape-open (LTO). LTO was developed in the late 1990s as an open-source alternative
to the various proprietary systems on the market. Table 7.7 shows parameters
for the various LTO generations.

## Slide 42: Summary
Chapter 7
Magnetic disk
  Magnetic read and write mechanisms
  Data organization and formatting
  Physical characteristics
  Disk performance parameters
Solid state drives
  SSD compared to HDD
  SSD organization
  Practical issues
  Magnetic tape
External Memory
RAID
  RAID level 0
  RAID level 1
  RAID level 2
  RAID level 3
  RAID level 4
  RAID level 5
  RAID level 6
Optical memory
  Compact disk
  Digital versatile disk
  High-definition optical disks
Notes: Chapter 7 summary.